| ECU | S40PRO | S60PRO | S80PRO | S100PRO | Notes |
| --- | --- | --- | --- | --- | --- |
| Size | 115 x 100 x 41 | 134 x 134 x 46 | 240 x 134 x 46 | 240 x 134 x 46 | Not Including Connector Clearance |
| Weight | 268g | 679g | 1130g | 1130g |  |
| Processor | ST 40MHz Risc | ST 40MHz Risc | ST 40MHz Risc | ST 40MHz Risc |  |
| Features | S40PRO | S60PRO | S80PRO | S100PRO |  |
| Max Cylndrs Coil per Plug | N/A | 4 | 8 | 10 | Complete range of engines covered |
| Max Cylndrs Sequential Inj. | N/A | 4 | 8 | 10 |  |
| Max Cyl. Wasted Spark | 4 | 8 | 12 | 12 |  |
| Max Cyl. Grouped Inj | 4 | 8 | 12 | 12 |  |
| Unequal Firing | N/A | Yes | Yes | Yes | For complex V engines |
| Turbo Control | Yes | Yes | Yes | Yes | Via PWM Valve |
| Idle Control | Yes | Yes | Yes | Yes | Via PWM Valve or Ignition Advance |
| Cam Control | No | Yes | Yes | Yes | Via PWM Valve or simple switcher |
| Auto Tune | Yes | Yes | Yes | Yes | For rapid calibration |
| Closed Loop Fuel | Yes | Yes | Yes | Yes | Excellent emissions performance |
| RPM Limit | 20000 | 20000 | 20000 | 20000 | Ideal for motorcycles |
| Twin Spark Engines | No | Yes | Yes | Yes | Porsche, Fiat etc. |
| Twin Injector Engines | Yes | Yes | Yes | Yes | Better than single very large injectors |
| Data Logging | No | Up to 8 Hrs | Up to 16 Hrs | Up to 16 Hrs | Flexible items and recording speed |
| Launch Control | Yes | Yes | Yes | Yes | Idiot proof starts |
| Traction Control | No | Yes | Yes | Yes | Adjustable from dashboard |
| Full Throttle Shift Cut | Yes | Yes | Yes | Yes | With 1 ms resolution variable for different gears |
| Twin Maps | No | Yes | Yes | Yes | Ideal as power switch in turbo installations |
| Engine Use Histogram | Yes | Yes | Yes | Yes | Engine builders dream record |
| Turbo Anti Lag | No | Yes | Yes | Yes |  |
| Crankshaft Oscilloscope | Yes | Yes | Yes | Yes | Tooth pattern and position calculated for fitters |
| Scaleable Sensors | Yes | Yes | Yes | Yes | Lots of preset options built in, fully customisable |
| Voltage Compensation | Yes | Yes | Yes | Yes |  |
| Flash Upgradeable | Yes | Yes | Yes | Yes | Keep up to date with latest features easily |
| CAN Network | Yes | Yes | Yes | Yes | Reliable and ideal for DTA Gdash |
| Flexible RPM Limit | Yes | Yes | Yes | Yes | Soft and hard |
| Flexible Input/Output | Yes | Yes | Yes | Yes | For user special requirements |
| Inputs | S40PRO | S60PRO | S80PRO | S100PRO |  |
| Throttle | Yes | Yes | Yes | Yes | 0 - 5 Volts |
| Water Temp | Yes | Yes | Yes | Yes | 2.4K Ohms nominal NTC |
| Air Temp | Yes | Yes | Yes | Yes | 2.4K Ohms nominal NTC |
| MAP | Yes | Yes | Yes | Yes | 0-5 Volts |
| Lambda | Yes | Yes | Yes (2) | Yes (2) | 0-5 Volts, twin lambda contr for V eng on S80/100 |
| Oil Pressure | Yes | Yes | Yes | Yes | 0 - 5 Volts, Warnings on dash if required |
| Fuel Pressure | Yes | Yes | Yes | Yes | 0 - 5 Volts, Warnings on dash if required |
| Oil Temp | Yes | Yes | Yes | Yes | 2.4K Ohms nominal NTC |
| Bat Volts | Yes | Yes | Yes | Yes | Internal |
| Wheel Speed | Yes (1) | Yes (1) | Yes (4) | Yes (4) | Hall effect NPN open collector |
| Inputs | S40PRO | S60PRO | S80PRO | S100PRO |  |
| Crank | VR | Hall & VR | Hall & VR | Hall & VR | Use original sensors |
| Cam | No | Hall & VR | Hall & VR x 2 | Hall & VR x 2 | Use original sensors |
| Spare Analogue | Yes(3) | Yes (3) | Yes (3) | Yes (3) | 0 - 5 Volts |
| Launch Switch | Yes | Yes | Yes | Yes | Momentary action push button |
| Shift Cut | Yes | Yes | Yes | Yes | Switch or NPN open collector |
| ALS/Second Map | No | Yes | Yes | Yes | Toggle Switch |
| Lambda Switch | No | Yes | Yes | Yes | Toggle Switch |
| Traction on | No | No | Yes | Yes | Toggle Switch |
| Traction Wet Dry | No | No | Yes | Yes | Toggle Switch |
| Uncommitted Switch | No | No | Yes | Yes | Toggle Switch |
| Outputs | S40PRO | S60PRO | S80PRO | S100PRO |  |
| Coils | 2 | 4 | 8 | 10 | 9 Amp |
| Injectors | 2 | 4 | 8 | 10 | 5 Amp |
| Tacho | Yes | Yes | Yes | Yes | 1 Amp |
| Fuel Pump Relay | Yes | Yes | Yes | Yes | 1 Amp |
| Shift Light | Yes | Yes | Yes | Yes | 1 Amp |
| Aux 2 / Fan | Yes | Yes | Yes | Yes | 1 Amp |
| Turbo Pressure | Yes | Yes | Yes | Yes | 1 Amp |
| Idle Speed | Yes (Shared Inj 2) | Yes | Yes | Yes | 1 Amp |
| Turbo ALS | No | Yes | Yes | Yes | 1 Amp (Shared Aux 4) |
| Cam Angle | No | Yes | Yes | Yes | 1 Amp (Shared Aux 1) |
| Other Aux | No | 3 | 5 | 5 | Flexible Switching Facilities |
| Other Features | S40PRO | S60PRO | S80PRO | S100PRO |  |
| Waterproof | No | Yes | Yes | Yes |  |
| Sealed latching connectors | Yes | Yes | Yes | Yes |  |
| Ign. only version available? | Yes | No | No | No |  |

Thanks to DTAfast for permission to use this information.